## Slide 1: Controlling cameras and motors with android phone
ESIEE-Paris Students: M. MARLEIX Mathieu Ms. VATON Doris
KOGAKUIN-University Supervisor: M. KANAMARU Takashi
Internship :
May 2012 – July 2012
&

## Slide 2: Plan of The Presentation
What is Shaipicku?
Recognition : Color & Shape
Arm : Controlled via Bluetooth
Configuration of The Board Game
How to Play Shaipicku?
Work’s Planification
Conclusion
Demonstration (Video)
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
&

## Slide 3: What is « Shaipicku »?
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
Game of Cubes
Two Cameras to Obtain a Full Image of the Board Game via WIFI
Five Motors to Have a Moving Arm to Pick Up the Cubes Controlled by Bluetooth
Four Modes to Play : « Color », « Shape », « Color & Shape » and « Pile-Up »
Two Methods to Play : « Button » or « Drawing »
&

## Slide 4: Recognition : Color & Shape
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
Software : Android 2.3.3 with The Library Open CV
  Color’s Recognition
   Why Color’s Recognition?
    Shape Recognition Required the Isolation of Objects on the Camera’s Image
 How is it performed?
    Use OpenCV HSV Color Space
    Closing to Reduce the Noise of the Image
H = HUE  Color
AFTER
BEFORE
H
S = SATURATION  Color’s Intensity
V = VALUE  Color’s Brightness
S
V
Closing
&

## Slide 5: Recognition : Color & Shape
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
  Form’s Recognition
   After Color’s Recognition :
  Object’s Color is White and Surroundings are Black
   First Step :
  Extracting the Edges
   Second Step :
  Calculation of the Following Ratio
  Metric_shape = Shape_Area * CShape/(Shape_Perimeter)²
  Perfect Shape  Metric_Shape = 1
  Deformed Shape Metric_Shape < 1
With
CCircle = 4*π CSquare = 16 Ctriangle = 18
Color
Edges
&

## Slide 6: Arm : Controlled via Bluetooth
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
Support
Motor 1
Motor 2
Motor 3
Motor 4
Motor 5
Arm: Kinematic Diagram
5 Motors for The Arm’s Movements
Right and Letf Movements -Motor 1
Up and Down Movements -Motor 2 & Motor 3 - Two Motors Increase the Scope
Pliers -Motor 4: Orientation of Pliers -Motor 5: Opening & Closing
The Pliers
&
Structure of the Arm

## Slide 7: Arm : Controlled via Bluetooth
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
&
The Control of The Arm
PWM Needed to Control the DC Motors of The Arm
 Use of a PIC to Have 5 PWM, One for Each Motor
Link Between the Phone and the Arm : Bluetooth Connexion
 Bluetooth Device Added to the RT-ADK Card
PIC24F on RT-ADK Mini Card
Bluetooth Transmiter
Bluetooth Connexion

## Slide 8: Configuration of the Board Game
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
Game Board : Top View
Cube 3
Cube 2
Cube 1
Figure 1
Figure 2
Figure 3
Camera 2
Camera 1
Robot Arm
&

## Slide 9: How to Play « Shaipicku »?
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
Mode : Shape
Mode : Color
Mode : Shape & Color
Mode : Pile-Up
Cube
Cube
Cube
Figure
Figure
Figure
Same Shape for Cube & Figure
Move To
Move To
Move To
Same Color for Cube & Figure
Same Shape & Color for Cube & Figure
1
2
3
1
2
3
Choice of The User
Order of The Cubes
Pile-Up
&

## Slide 10: Work’s Planification
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
&

## Slide 11: Conclusion
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
&

## Slide 12: Demonstration
SHAIPICKU / May 2012 - July 2012
MARLEIX Mathieu – VATON Doris
Video
&

## Slide 13: Questions ?
Shaipicku
ESIEE-Paris Students: M. MARLEIX Mathieu Ms. VATON Doris
KOGAKUIN-University Supervisor: M. KANAMARU Takashi
Internship :
May 2012 – July 2012
&